## Slide 1
An Open Geospatial Infrastructure for Ultra-High-Resolution River Imagery
and Geomorphological Annotations
Tulio Soto Parra, Luka Čehovin Zajc
2nd SMASHING WORKSHOP, Vipava, 2026
Notes: Good morning. Today I will present RiverTiles, an open geospatial platform for hyperspatial river imagery and geomorphological annotations. I want to start from a practical observation. In my still limited experience with geomorphological studies, I have repeatedly come back to the same issue: scale is often one of the main limiting factors. What we can say about a river is strongly conditioned by the data we are able to collect, at the spatial resolution, extent, and timing we need. Over the last five or six years I have been flying drones for river surveys, and I have seen this technology evolve very quickly. Drones became smaller, sensors improved, flight autonomy increased, and even the practical and legal side of flying has become more manageable in many contexts. So today, collecting centimeter-scale imagery of rivers is no longer exceptional. The potential for river science is huge, and UAV imagery is already widely used in geomorphology. But while data acquisition has evolved quickly, the tools for organizing and analyzing these data efficiently have not evolved at the same pace. RiverTiles is a small initial step in that direction.

## Slide 2
MOTIVATION
Scale determines what we can see
10²–10⁵ KM²
Catchment
→
10⁻¹–10¹ KM
Reach
→
10⁰–10² M
Geomorphic unit
→
10⁻¹–10¹ M
Hydraulic unit
→
10⁻²–10⁰ M
River element
Sediment dynamics
UAVs already resolve the finest scales.
Hydrological dynamics
Riparian dynamics
Hydraulic variability
Habitat
structure
Channel morphodynamics
Morphological diversity
The bottleneck shifted
Acquiring hyperspatial river data is no longer the hard part.
These surveys stay private, unlabelled, and described in incompatible terms, so almost none of them can be compared with each other.
Tulio Soto Parra | Vipava, 19.10.2026
Notes: To explain the motivation behind RiverTiles, I want to start with scale. Rivers are hierarchical systems: we can study them at the scale of a catchment, a river corridor, a reach, a geomorphic unit, or even a sediment patch or piece of large wood. The type of question we can ask depends strongly on the scale and resolution of the data. At coarse resolution we can describe broad channel patterns or regional changes, but we cannot reliably identify small bars, secondary channels, wood accumulations, vegetation dynamics, or local sediment structures, which is why processes at smaller scales are much difficult to study. This is why hyperspatial imagery is so attractive for river science: it lets us observe the river at the scale where many geomorphological and ecological processes are actually expressed. Scale is also about extent and timing, not only resolution. Ideally data are detailed enough, cover enough of the corridor, and can be repeated after floods, restoration interventions, or low-flow periods. And here is the point I want to leave you with before the next slide. Acquiring this kind of data is no longer the hard part. Drones are cheap, photogrammetry is routine, and I would guess that many of you in this room have flown a river reach at centimetre resolution in the last year or two. Collectively, our community has already surveyed an enormous amount of river.
But almost none of it is used twice. Those surveys sit on institutional drives and personal disks; they are rarely published, because there is nowhere natural to publish them. When they are published, they come without enough context, an orthomosaic alone tells you very little unless you already know that river. And when they are annotated, everyone uses their own classes and their own definitions, so two datasets cannot be compared even when both are open.
So the limitation in hyperspatial river science today is not resolution, and it is not volume. It is that we cannot see each other's rivers, and when we can, we cannot compare them. Every study starts from zero. We have thousands of excellent local case studies and almost no way to generalize across them.
That is the gap RiverTiles was built to close.

## Slide 3
THE PROJECT
rivertiles: an open geospatial platform for hyperspatial river data
A platform to publish ultra-high-resolution river imagery and its geomorphological annotations.
01
Open, with credit
Data available to everyone;
and attributed to the people who collected it
02
A shared vocabulary
One catalog of geomorphological classes, applied the same way at every site.
Tulio Soto Parra | Vipava, 19.10.2026

## Slide 4
ANNOTATION FRAMEWORK: A SHARED VOCABULARY
A hierarchy built on the Geomorphic Units Survey
and Classification System
(Fryirs and Brierley, 2013; Belletti et al. 2017)
Tulio Soto Parra | Vipava, 19.10.2026
Notes: To organize these data scientifically, RiverTiles uses the hierarchical logic of the Geomorphic Units Survey framework proposed by Belletti et al. 2017. At the broadest level, we annotate macro-units such as water edge, exposed sediment, and vegetation, directly visible in RGB orthomosaics. At an intermediate level, the framework includes geomorphic and hydromorphological units such as riffles, pools, bars, islands, side channels, and backwaters. At finer levels it includes localized features such as gravel patches, boulders, large wood accumulations, rootwads, and anthropogenic structures. The important point is that this is not a rigid taxonomy applied blindly. Some classes are directly observable, while others require expert interpretation, terrain information, flow context, or field validation.
RiverTiles therefore applies the hierarchy at the finest reliable level supported by the available data.

## Slide 5
DATA CURATION
How a dataset gets in
1
Contributed
River surveys are contributed by researchers, practitioners and organizations collecting geospatial data on rivers.
Curated & annotated
Datasets are standardized using a shared geomorphological dictionary.
Published & preserved
Each dataset is published in rivertiles with complete metadata and contributor attribution.
2
3
From river survey to shared dataset.
Every contribution is checked, documented and made ready for reuse.
Tulio Soto Parra | Vipava, 19.10.2026
Notes: So how does a dataset make its way into RiverTiles? This slide is really about the curation workflow
It starts with the community. The datasets come from researchers, practitioners, and organizations already collecting drone imagery over rivers. Currently, contributions happen through direct collaboration with us but we’re on our way of implementing a user-authenticated uploads
The second step is annotation. The imagery is annotated using a shared geomorphological dictionary, with features delineated manually or with AI assistance and checked for consistency. This is what makes a pool, a riffle, or a gravel bar mean the same thing across different rivers, so the datasets become directly comparable.
Finally, every dataset is documented and published. We register the acquisition details, coordinate reference system, licence, contributors, and other metadata, and the dataset is published in RiverTiles with full attribution. If it hasn’t already been deposited elsewhere, we also archive it in our Zenodo community so it receives a DOI and can be cited independently.
The goal is that every dataset follows the same workflow before it reaches the archive. That takes a bit more effort, but it means the data are consistent, well documented, and ready to be reused by others.

## Slide 6
WHAT IT ENABLES
Scientific opportunities
Comparative river research
Comparing geomorphic structure across river types, regions, or environmental gradients.
Deep learning for river mapping
Using the annotated archive to train models that automatically recognize and map river features.
Reproducible benchmarking
Common reference datasets for comparing methods across studies.
Cross-scale analyses
Connecting centimetre-scale UAV observations with broader satellite observations.
Tulio Soto Parra | Vipava, 19.10.2026
Notes: Cover scientific and machine-learning opportunities: comparative research, multi-temporal analysis, and benchmark datasets.

## Slide 7
THE PLATFORM
Map and data filtering
Data viewer
Elevation layer rendering
Annotation overlays
Tulio Soto Parra | Vipava, 19.10.2026
Notes: Walk through the interactive interface: map exploration, orthophoto view, DEM visualization, and hierarchical annotation overlays.

## Slide 8
CURRENT SCALE
The repository today
60
Orthomosaic datasets
25
Terrain products
34
River reaches
6
Countries
+150 GB
Raster data hosted
Spatial resolutions from 0.5–5 cm GSD, across braided alpine rivers, restored lowland channels, and gravel-bed systems.
Tulio Soto Parra | Vipava, 19.10.2026
Notes: Give the scale of the current repository: 35 orthomosaic datasets, 22 terrain products, 14 reaches, 5 countries, 1.8 TB.

## Slide 9
OUTLOOK
Toward a growing river-science infrastructure
lives and grows through its community. Join us and become part of it.
Explore the platform
and contribute
Tulio Soto Parra
t.sotoparra@fri.uni-lj.si
visit rivertiles.org
Supported by the European Union's Horizon Europe research and innovation programme under the Marie Skłodowska-Curie Postdoctoral Fellowship Programme (SMASH, Grant Agreement No. 101081355).
Notes: Good morning. Today I will present RiverTiles, an open geospatial platform for hyperspatial river imagery and geomorphological annotations. I want to start from a practical observation. In my still limited experience with geomorphological studies, I have repeatedly come back to the same issue: scale is often one of the main limiting factors. What we can say about a river is strongly conditioned by the data we are able to collect, at the spatial resolution, extent, and timing we need. Over the last five or six years I have been flying drones for river surveys, and I have seen this technology evolve very quickly. Drones became smaller, sensors improved, flight autonomy increased, and even the practical and legal side of flying has become more manageable in many contexts. So today, collecting centimeter-scale imagery of rivers is no longer exceptional. The potential for river science is huge, and UAV imagery is already widely used in geomorphology. But while data acquisition has evolved quickly, the tools for organizing and analyzing these data efficiently have not evolved at the same pace. RiverTiles is a small initial step in that direction.

## Slide 10
TECHNICAL ARCHITECTURE
Gigabyte-scale imagery, served on demand
01
Browser Client
React, Vite and MapLibre GL. Pan, zoom, toggle layers; nothing to install.
02
Tile service - TiTiler
Cuts the requested piece of the image at the requested zoom, on the fly.
03
Storage - COG repository
Cloud Optimized GeoTIFFs on S3-compatible object storage.
Add note
04
Metadata registry - STAC
Describes what each dataset is, where and when it was flown, and who contributed it.
Notes: A quick word on how this works under the hood. The problem is simple to state. A single orthomosaic of one river reach at centimetre resolution is several gigabytes. You cannot send that to a browser. The classical solution is to pre-cut the whole image into millions of small tiles in advance, which is slow, and has to be redone every time a dataset is added or changed.
RiverTiles does it the other way around, and the chain has four links. At the front is the browser client React, Vite, MapLibre. That is what you see: pan, zoom, switch layers on and off. Nothing to install, no GIS software, it runs on a laptop or a phone.
When you move the map, the client asks a tile service: TiTiler, for exactly the piece of image it needs at the zoom level you are looking at. TiTiler cuts that piece on the fly. Nothing is prepared in advance.
It cuts it from the storage layer, where the imagery sits as Cloud Optimized GeoTIFFs on S3-compatible object storage. The trick of that format is that the file is internally organized so you can read a small window out of a huge image without downloading the rest. So a five-gigabyte mosaic costs you a few hundred kb to look at.
And alongside it there is a metadata registry, following the STAC standard, which records what each dataset is, where and when it was flown, and who contributed it. That is what makes the archive searchable rather than just a folder of files.
The practical workflow for you adding a new dataset means uploading the file and its metadata. No tile generation, no pipeline to rerun.

## Slide 11
THE DATASET PACKAGE
What a rivertiles dataset contains
RGB orthomosaic
Centimeter-scale visual base layer
Aurino-Ahr River, Austria
Wandering, multi-thread, gravel-bed
Farò et al. 2025, WIREs WATER
Avisio River, Italy
Restored reach, multi-thread, gravel-bed
Soto Parra et al. 2025, Hydrological Processes
Annotation layers
Detailed metadata
Hierarchical GUS classes
Hydromorphological information, flight details, citation
Tulio Soto Parra | Lausanne, 17.08.2026
Notes: And this is what you actually get when you open a RiverTiles dataset.
At the core is the RGB orthomosaic. This is the original centimetre-scale imagery, which is the visual representation of the river reach,f rom which everything else is built. At this resolution you can distinguish boundaries, vegetation patches, woody debris, and many other geomorphic features.
On top of that comes the annotation layer. These are the mapped geomorphic classes, following the shared hierarchy I introduced earlier. Because the imagery and the annotations are co-registered, you can immediately use them for visualization, quantitative analysis, or as training data for computer vision models.
The third component is the metadata. Every dataset includes detailed information about the acquisition itself,things like the platform, coordinate reference system, georeferencing method, spatial resolution, as well as hydromorphological descriptors of the river, contributor information, licensing, and citation details.
Together, these three components form a complete dataset package: the imagery, the interpretation of that imagery, and the information needed to understand, reproduce, and properly reuse the data.