## Slide 1
Integrating Photo-Thermal Aerosol Absorption Monitor and Single-Particle Spectroscopy with Machine Learning to Improve Mass Absorption Cross-Section Measurements of Black Carbon and Mineral Dust Aerosols
Speaker: Dr. Ankur Bhardwaj
Centre for Atmospheric Research, UNG
(ankur.bhardwaj@ung.si)

## Slide 2
The Critical Role of BC and Mineral Dust
1
Long-Term Climate Trends: A 2026 study in Nature (Vasilakos et al.) reveals that ground-level dust concentrations rose significantly across Europe between 2012 and 2021. The research links these intensified North African dust intrusions to shifting atmospheric circulation and accelerating land degradation in a changing climate, warning of increasing risks to public health and air quality.
Extreme Events & Pollution: A 2024 study in Atmospheric Chemistry and Physics (López-Darias et al.) documents how unprecedented Saharan dust events are expanding northward over the Atlantic and Europe, causing record-breaking particulate matter pollution episodes.
Notes: Mineral dust is a primary atmospheric aerosol made of tiny mineral particles. It typically consists of crustal minerals such as silicates, oxides, and carbonates. (Quartz (SiO₂), aluminosilicate clays, iron oxides, calcium carbonate (CaCO₃), and other oxides/carbonates).
Need for Accuracy: Current measurement methods have significant limitations, such as scattering artifacts in filter-based measurements and morphological assumptions in single-particle methods. More accurate, in-situ MAC measurements are needed to constrain aerosol light absorption in climate models.
It has a significant impact on Earth's radiative balance
The Mass Absorption Cross-section (MAC) of dust is highly variable, typically ranging from 0.01 to 0.1 m²/g at 550 nm. This large variability is primarily due to diverse mineral compositions and size distributions. 3.

## Slide 3
SP2 and PTAAM Instrument’s Working and ML
2
Notes: Working Principle SP2: The SP2 uses laser-induced incandescence and scattering to detect and size individual black carbon-containing particles. This yields detailed information on particle mixing state and size distribution.
Working Principle: The PTAAM utilizes photothermal interferometry (PTI) with modulated continuous-wave lasers (from blue to infra-red wavelengths) as excitation sources and a red laser () as a probe beam. Absorption of the excitation beam by aerosols induces a phase shift in the probe beam, which is then measured to quantify absorption. Key Advantage: The PTI signal is independent of the absorbing aerosol size and is insensitive to aerosol scattering. This makes it highly valuable for measuring weakly absorbing aerosols like dust without the artifacts common to filter-based methods.
Working Principle SP2: The SP2 uses laser-induced incandescence and scattering to detect and size individual black carbon-containing particles. This yields detailed information on particle mixing state and size distribution.
Working Principle: The PTAAM utilizes photothermal interferometry (PTI) with modulated continuous-wave lasers (from blue to infra-red wavelengths) as excitation sources and a red laser (𝜆=633 𝑛𝑚) as a probe beam. Absorption of the excitation beam by aerosols induces a phase shift in the probe beam, which is then measured to quantify absorption. Key Advantage: The PTI signal is independent of the absorbing aerosol size and is insensitive to aerosol scattering. This makes it highly valuable for measuring weakly absorbing aerosols like dust without the artifacts common to filter-based methods.

## Slide 4
Preliminary Results: Sonipat Campaign, India
3
The mass density is distributed significantly below the 1:1 () line, indicating heavily coated or internally mixed particles.
The primary density mode shifts upward toward the 1:1 line (confirming the evaporation of volatile coatings), a distinct, dense plume remains entrenched far below the 1:1 line.
This persistence of solid, highly refractory organic mass validates the presence of tarballs or mineral dust within the plume
Notes: To definitively separate tarballs from mineral dust, you cannot rely solely on CPMA mass and simple incandescence. You must look at the color temperature of the incandescence. The SP2 uses broadband and narrowband detectors; black carbon and charred organic tarballs vaporize and incandesce at ~4000 K, while metal-containing mineral dusts (like iron oxides) incandesce at significantly lower temperatures. If the SP2 data indicates a shift in the broadband-to-narrowband incandescence ratio for this specific plume, it is mineral dust. If the color temperature matches canonical soot/charred organics, it is tarball mass.
Working Principle SP2: The SP2 uses laser-induced incandescence and scattering to detect and size individual black carbon-containing particles. This yields detailed information on particle mixing state and size distribution.
Working Principle: The PTAAM utilizes photothermal interferometry (PTI) with modulated continuous-wave lasers (from blue to infra-red wavelengths) as excitation sources and a red laser (𝜆=633 𝑛𝑚) as a probe beam. Absorption of the excitation beam by aerosols induces a phase shift in the probe beam, which is then measured to quantify absorption. Key Advantage: The PTI signal is independent of the absorbing aerosol size and is insensitive to aerosol scattering. This makes it highly valuable for measuring weakly absorbing aerosols like dust without the artifacts common to filter-based methods.

## Slide 5
4

## Slide 6
Thank you for your attention